## Slide 1
CONTINUUM CROWD DYNAMICS
Room Evacuation Problem
UGP Presentation
Ananya Narayani

## Slide 2
Introduction
Room evacuation studies the movement of a crowd from an enclosed space through available exits.
Evacuation efficiency depends on factors such as crowd density, pedestrian movement and exit configuration.
At high densities, pedestrian interactions can lead to congestion and slower evacuation.
A continuum crowd model can represent the crowd through its density and velocity fields, providing a computationally efficient way to study large crowds.
The present work focuses on applying this framework to a room evacuation problem and investigating the effect of multiple exits on evacuation time.
3

## Slide 3
PAPER 1
Hughes' continuum theory of pedestrian flow
• Treats a crowd as a “thinking fluid” governed by a conservation law for density ρ(x,y,t) • Direction of travel comes from a potential field: pedestrians choose the path of least instantaneous cost, not shortest distance • Identifies two flow regimes — subcritical (dense, fills all available space) and supercritical (can self-confine) • Validated qualitatively against aerial observations of pilgrim flow at the Jamarat Bridge, Mecca
The crowd is treated as a continuum, similar to a compressible fluid.
Density, represents the number of pedestrians per unit area.
The pedestrian velocity depends on:
Local crowd density
Walking speed
Direction of movement
Travel cost towards the destination
3
Hughes, R. L. (2002). A continuum theory for the flow of pedestrians. Transportation Research Part B: Methodological, 36(6), 507–535.

## Slide 4
PAPER 2
An efficient solution algorithm for Hughes' model
• Reformulates Hughes’ model and connects it to reactive dynamic user equilibrium: each pedestrian minimizes their own instantaneous travel cost • Proposes a concrete numerical scheme: WENO for the conservation law + Fast Sweeping Method for the Eikonal (potential) equation • Demonstrates the algorithm on a numerical benchmark — a corridor with an obstacle, two exits, and a time-varying inflow pulse
Continuum Crowd Dynamics — UGP Progress
4
Huang, L., Wong, S. C., Zhang, M., Shu, C.-W., & Lam, W. H. K. (2009). Revisiting Hughes’ dynamic continuum model for pedestrian flow and the development of an efficient solution algorithm. Transportation Research Part B: Methodological, 43(1), 127–141.

## Slide 5
THE MODEL
Governing equations
CONSERVATION LAW
∂ρ/∂t + ∇·(ρv) = 0
Density ρ(x,y,t) is neither created nor destroyed — it only redistributes through the velocity field v.
SPEED LAW
v(ρ) = 2 (1 − ρ/10)
Walking speed falls off linearly with local density, reaching zero at the maximum packing density.
EIKONAL EQUATION
|∇φ| = cost(ρ)
φ is a travel-cost potential toward the nearest exit; pedestrians always move down its steepest gradient.
COST FUNCTION
cost = 1/v(ρ) + discomfort(ρ)
Combines slowdown from crowding with an explicit “crowding penalty” that discourages dense regions.
5

## Slide 6
THE MODEL
Numerical method: two coupled solves per timestep
1. Compute fields
speed(ρ), discomfort(ρ), cost(ρ) from current density
2. Solve Eikonal eqn.
1st-order Godunov fast sweep → refined by high-order WENO fast sweep
3. Get velocity field
v = speed · (−∇φ / |∇φ|), CFL-based adaptive Δt
4. WENO5 flux (space)
5-point reconstruction with Lax–Friedrichs flux splitting at each cell face
5. SSP-RK3 (time)
3-stage strong-stability-preserving Runge–Kutta update for ρ
6. Boundary + repeat
Apply exit/wall boundary conditions, extrapolate ghost cells, advance t
6

## Slide 7
VALIDATION
Benchmark problem: reproducing Huang et al. (2009)
Obstacle
Exit 1
Exit 2
IN
Pedestrian inflow enters at the left wall (pulse, t = 0–120s) • Exits on the right wall
100m × 50m corridor
• Domain: 100m × 50m corridor, zero initial density • One rectangular obstacle placed centrally, blocking the direct path • Two exits on the right wall • Unsteady inflow at the left wall: ramps up for 60s, back down over the next 60s, then stops — modelling a pulse of arriving pedestrians
7

## Slide 8
VALIDATION
Benchmark problem: reproducing Huang et al. (2009)
IN
Pedestrian inflow enters at the left wall (pulse, t = 0–120s) • Exits on the right wall
100m × 50m corridor
Observation:
The crowd flow splits around the central obstacle and converges towards the available exits
7

## Slide 9
NEW SCENARIO
Extending the model: single-room evacuation
With the solver validated, I moved to a second, practically-motivated scenario: how many exits does a room need to evacuate quickly?
Crowd block
(100m × 50m)
N doors, width D,
equally spaced
100m × 100m room
• Room: 100m × 100m, initially empty • Crowd occupies the right half (100m × 50m block) at a chosen density • N equally-spaced exits of width D on the left wall • Problem: How does evacuation time change as N (number of doors) varies? Make a final graph with total evacuation time with number of doors
9

## Slide 10
Parameters:

## Slide 11
DESIGN CONSTRAINTS
What bounds the range of N tested?
NO-CHOKING CONDITION
N · D · 5 ≥ 100 · ρ
Total exit throughput (doors × width × max flux) must meet or exceed crowd demand — otherwise density piles up faster than doors can drain it.
With D = 15m, ρ = 1: this requires N ≥ 2 — which is why the sweep starts at N = 2, not N = 1.
GEOMETRIC FIT CONDITION
N · D ≤ wall length
The doors must physically fit along the wall without overlapping — the code enforces this and errors out if violated.
With D = 15m on a 100m wall: N ≤ 6 — which sets the upper end of the sweep.
Continuum Crowd Dynamics — UGP Progress
11

## Slide 12
RESULTS
Evacuation time vs. number of doors
Observations:
Total evacuation time is decreasing with increasing the number of doors.
12
N_doors EvacTime_s
2 70.21
3 58.44
4 55.75
5 55.67
6 55.00

## Slide 13
RESULTS
Density state, by number of doors
N = 2
N = 3
N = 4
N = 5
N = 6
13

## Slide 14
RESULTS
Simulation for N=2
13

## Slide 15
Future Work
15
Study the effect of different crowd densities on evacuation time.
Vary the door width and analyze its influence on evacuation efficiency.
Induce some obstacles in between the room
Perform simulations with a different number of doors.
Calculate the total evacuation time for each door configuration.
Plot Evacuation Time vs. Number of Doors to study the effect of increasing exits.
Compare the results for different densities and door widths to identify their influence on evacuation performance.
Analyze the effectiveness of additional exits and identify the point beyond which adding more doors provides limited improvement.

## Slide 16
REFERENCES
References
[1]
Hughes, R. L. (2002). A continuum theory for the flow of pedestrians. Transportation Research Part B: Methodological, 36(6), 507–535.
[2]
Huang, L., Wong, S. C., Zhang, M., Shu, C.-W., & Lam, W. H. K. (2009). Revisiting Hughes’ dynamic continuum model for pedestrian flow and the development of an efficient solution algorithm. Transportation Research Part B: Methodological, 43(1), 127–141.
15

## Slide 17
Thank you